433MHz Wireless Exit Button

User Manual

1. Introduction

It is a 433MHz wireless exit button, with 1 million groups of rolling code encryption, secure and reliable.

2 versions are available:

Wet contact control - no isolation to the circuit, control current ≤3A.

Dry contact control - with isolation circuit, control current ≤5A, can connect with household electrical appliances or lock to control directly.

2. Specifications

| Operating Voltage Wireless Exit Button Control panel | 2032 3V Li-battery DC 12±20% |
| --- | --- |
| Current Idle Current Working Current | Wireless Exit Button: ≤5uA; Control Panel: ≤20mA Wireless Exit Button: ≤8mA; Control Panel: ≤60mA |
| Communication Frequency | 433MHz |
| Communication Distance | About 50m |
| Relay Contact Load | Wet contact control: ≤3A; Dry contact control: ≤5A |
| Environment Operating Temperature Operating Humidity | -20(C～+60(C 0%～86% |

3 Application

3.1 Wet Contact Control

Remark: “ON/OFF” represents “Toggle Mode”

| PIN | Notes |
| --- | --- |
| +12V | Positive Pole of Control Panel’s Power Input |
| GND | Negative Pole of Control Panel’s Power Input |
| CONTROL | Control PIN (Low Level effective) |

3.2 Dry Contact Control

Remark: “ON/OFF” represents “Toggle Mode”

| PIN | Notes |
| --- | --- |
| +12V | Positive Pole of Control Panel’s Power Input |
| GND | Negative Pole of Control Panel’s Power Input |
| NC | Normally Closed Relay Output |
| COM | Common Connection for Relay Output |
| NO | Normally Open Relay Output |

- Dimensions

5. How to pair and clear pairing

5.1 Pair Wireless Exit Button and Control Panel

Remark: 1 Control Panel can pair with 6 Wireless Exit Buttons

Control Panel: Press the button “Pair” for 3 seconds, then the indicator light stays on

Wireless Exit Button: Press exit button once, the LED light shines, then they pair successfully.

5.2 Clear Pairing

Press the control panel’s button “Pair” for 5 seconds, the indicator light shines quickly, then clear

Pairing successfully.